TREATMENT SETTINGS – ALEX/YAG

GOAL – Hair Free in 3-4 Treatments!!

DO NOT BURN PATIENTS – Burn prevention protocol supersedes everything!!

SHavE thoroughly – Prevent Singing & Window Damage

CLEAN TX AREA THOROUGHLY – No Makeup, Deodorant, Moisturizer

PRE & POST-ICE – For Pain and Better Results

LHR  ALEX/YAG

| Skin Type | Machine | SPOT SIZE | Tx #1 | Tx #2 | Tx #3 | Tx #4 & Up | DCD |
| --- | --- | --- | --- | --- | --- | --- | --- |
| I-II | ALEX | 18 | 18 | 20 | 20 | 15mm/24j | 30/20/0 |
| III | ALEX | 18 | 16 | 18 | 20 | 15mm/24j | 30/20/0 |
| IV | YAG | 15 | 36 | 40 | 44 | 44 OR Call Dr K | 30/20/0 |
| V | YAG | 15 | 30 | 32 | 38j/ 30msec | 38j/ 30msec | 30/20/0 |
| VI | YAG | 18 | 26 | 28 | 30 | Call Dr K | 30/20/0 |

| Neck / BBE (Labia only) | ALEX | 18mm | 12j |  |  | 30/20/0 |
| --- | --- | --- | --- | --- | --- | --- |
| Neck / BBE (Labia only) | YAG | 18mm | 24j |  |  | 30/20/0 |

Spider Veins Quantum - Nd:Yag

| Program | Tx #1 | Tx #2 | Tx #3 |
| --- | --- | --- | --- |
| Program Type II | 120 | 140 | 160 |